## Slide 1: VARIATIONS OF PULKOVO COORDINATES V.Gorshkov, N.Miller, E.Prudnikova, N.Shcherbakova, V.Naumov, V.Vorotkov Laboratory of Geodynamics of Pulkovo observatory
<footer>
<date/time>
This research was motivated by the next dates of our observational history:
100 years of latitude observations by Freiberg zenith telescope (ZTF-135),
80 years of Greenwich-Pulkovo longitude determination by Beliaev and Dneprovsky,
50 years of permanent Universal Time (longitude) observations by photoelectric transit instruments.
The second reason was new and large ICRS (HiC, ACT and AriHip) catalogues and the new precession-nutation model IAU2000, which takes into account all relativistic effects. And the third reason was our database of initial observation (http://www.gao.spb.ru/russian/lg/database.html) that allows to reprocess easy series in any new model.
Observational statistics of latitude (ZTF-135, ZTL-180) and time (PUF, PUG, PUH) instruments
 | PUF (W) | PUG (E) | PUH (W) | ZTF-135 | ZTF-135 | ZTL-180
Span & mean epoch | 1961.1-1971.4 1967.1 | 1971.2-1985.4 1977.8 | 1971.8-2003.0 1987.4 | 1904.7-1941.5 1923.1 | 1948.7-2003.8 1978.8 | 1967.4-1974.7 1971.1
Stars (days) | 43918 (992) | 61772 (1523) | 133201 (3304) | 55199 (4131) | 102018 (7350) | 8020 (571)
Sint/Sext (mas) | 150 222 | 156 180 | 184 217 | 166  149 | 185 171 | 202 147
The internal standard deviations of stars (Ss) were reduced to the equator and zenith of observatory by Sint = Ss cosδs (cosz)p, where p (~0.5) is a parameter estimated by least square method from each series. The external accuracy (Sext) was obtained as residuals from global solutions of Earth orientation parameters EOP(IERS)C01 for latitude (RF) and C04 for longitude (RT).

## Slide 2
Behavior of instrumental longitudes ( RTi )
Longitude corrections (Δλ) gives on 2000.0
RTi = (UT0i –UTC) (UT1RUTC) – (Xsin0+Ycos0)tg 0/15
The nonpolar latitude variations, their linear
approximation and long-periodical trend RFi = (φ –φ0) - (Xcos0 - Ysin0)
SPAN | 2000.0 (mas) | d/dt (mas/year)
1904 - 1941 (ZTF135) | 102 ± 22 | -0.032 ± .029
1948 - 2003 (ZTF135) | 95.9 ± 5.1 | -0.028 ± 0.018
1904 - 2003 (ZTF135) | 90.1 ± 3.8 | -0.031 ± .071
(SSA- singular spectrum analysis -http://www.gistatgroup.com/gus/book2/index.html

## Slide 3
<footer>
<date/time>
      Reanalysis of 1925 year series
28 days,
Belyaev-Creenwich 18.5637 ± .0035
Dneprovsky-Pulkovo
36days,
Belyaev-Pulkovo
Dneprovsky-Greenwich 18.5577 ± .0038
Mean 18.5607
New estimation for 2000.0
The estimation of longitude
for last 45 years
by three PTI 2h 01m 18.5616s ± .0024
Weighted mean of Pulkovo longitude trend
d/dt = 0.45  0.10 msec/year
(d/dt = 103  22 mm/year).
The estimation of latitude
for last 100 years 590 46‘ 18.656“ ± .006
Linear trend of ZTF-135 latitude
dφ/dt = - 0.031  0.071 mas/year ( - 1 mm/year)

## Slide 4
Analysis of time observations
As we can see PTI observations have oscillations of UT1-UTC about 6-7 years. It is large enough component and it can not be explained by any catalogues and observation errors, which usually have seasonal variations. These variations are present in EOP solution from the best astrometric instruments of XX century (Vondrak et al, 1998, Publ. Astr. Inst. Acad. Science of Czech Rep, N87, pp. 53). These plots show the same variation which we revealed in EOP(IERS)C04 series and in the long series of length of day (LOD) variations from IERS site (http://hpiers.obspm.fr/eop-pc/products/longterm/) by using singular spectrum analysis (SSA).
In the left plot there are original UT (upper plot) & LOD (middle plot) series from EOP(IERS)С04 and its low frequency & annual SSA approximations (residuals between them gives in the lower plot in enlarged scale). In the right plot there are long series of LOD (upper plot), low frequency SSA approximations of LOD (middle plot) and residuals between them (lower plot).

## Slide 5
We try to find some geophysical explanation of these LOD oscillations. There is most evident similarity of these oscillations with pulses of annual (an) and chandler (ch) combination of polar motion (left plot). We construct the function [COV]=d(an)/dt*d(ch)/dt, which describes the modulation envelope of these oscillations. As shown in the right plot these processes coinside during whole XX century with specific details. So evidently that when polar oscillations (annual and chandler) are in phase the LOD increases and vice versa. In other words when polar components are in phase then the speed of Earth rotation decreases, and when ones in counter motion – the speed of Earth rotation increases.
It can be marked that quasi-six-year oscillations of LOD practically vanished after 1986 when modern (GPS, VLBI and SLR) tools started observations. So it means that these LOD oscillations are mainly the plumb line oscillations and therefore they maybe reflect variations of gravitation potential. These potential variations caused for example by the interactions of internal shells of the Earth reacting nonlinearly on the phase correlation of seasonal and chandler polar variations (Gorshkov V., Vorotkov М., 2002, Izvest. GAO, N216, pp. 415-425 (in Russian).

## Slide 6
Analysis of latitude observations
The ZTF-135 latitudes were jointed in normal points with the step of 0.05 year and the gap caused by war was filled by the values from global solutions EOP(IERS)C01. So we obtained the unbroken series. It permitted to investigate long-periodical latitude variations during last 100-years.
In the left plot are given the mean latitude variations by SSA, Orlov filter and its long-periodical variations.
In the right plot are shown first three SSA components of long-periodical variations of the mean latitude.

## Slide 7
The second and the third components of latitude variations have the periodical character near to the well known solar activity period but in opposite phase as it can be seen in the left plot. We placed here scaled (1:2000) Sun spot number (SSN) and second and third SSA components of latitude variations. The direct FFT filtering (0.06 - 0.20 cpy) of inverted latitude variations are compared also with SSN and scaled cosmic rays data from Climax station in right plot. Very likely that the solar activity shows itself in systematic influence on local conditions of latitude observations. For instance, solar activity can influence on latitude variations by the temperature inversions in the atmosphere which can cause local refraction anomalies.